## Slide 1: Remote Heart Rate Estimation Based on 3D Facial Landmarks
Yuichiro Maki1, Yusuke Monno1, Masayuki Tanaka1,2, and Masatoshi Okutomi1
1Tokyo Institute of Technology 2National Institute of Advanced Industrial Science and Technology
International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC2020)

## Slide 2: Background
Remote HR measurement from a facial video
- Non-contact measurement
- Low-cost and instant measurement
- Multiple subjects measurement
Facial video
Blood volume pulse (BVP)
Cardiac information
- Heart rate (HR)

## Slide 3: Contributions
We proposed a HR estimation method based on 3D facial landmarks.
  Increase HR estimation accuracy based on 3D facial visibility check.
  Enable to estimate HR even in facial-skin-occluded situations.
We have launched a publicly available HR estimation code.
Previous research
Our research
Considered range
of applications
Large head rotations
Small head rotations

## Slide 4: 2D and 3D facial landmark detection
 | 2D facial landmark detection | 3D facial landmark detection
Represented coordinate | (x, y) image coordinate | (x, y) image and depth (z) coordinate
Facial skin occlusion | Not considered | Considered
Reference code | Nirkin et al., FG, 2018 [15]. | Bulat et al., ICCV, 2017 [13].
2D facial landmark detection
3D facial landmark detection

## Slide 5: 2D and 3D facial landmark detection
Limitations of 2D facial Landmarks: Weak to head rotations
Landmarks have no consistency.
Detection failure
Detection lost
No consistency
Failure
Lost
3D facial landmarks detection overcomes
such limitations.
Success
Success

## Slide 6: Our method flow
Input video
3D facial landmarks
Temporal
smoothing
Smoothed 3D
facial landmarks
Framewise visibility
check
3D facial
landmarks detection
Patch visibility:
Visible or Invisible
ROI
definition
ROI-defined
video
Time-window visibility
check
Face patch visibility mask
HR
ICA-based HR estimation (Existing approach)

## Slide 7: Temporal smoothing
Reduce the fluctuations of the 3D landmarks.
: Range of smoothing (=3 in our paper)
: Location of the landmarks
Original landmarks
Smoothed landmarks
Framewise visibility check
Temporal smoothing
Time-window visibility check

## Slide 8: Framewise visibility | Face patch generation
Define left and right cheek region (Drawn with gray bold lines) Each region is defined by the seven landmarks.
Patch division (Drawn with gray thin lines) Each cheek region is divided into 3D patches by the 44 uniform grid.
Framewise visibility check
Temporal smoothing
Time-window visibility check

## Slide 9: Framewise visibility | Patch visibility calculation
Calculate the normal of each patch (Drawn with black arrows)
Calculate the angle between patch normal and z-axis
Framewise visibility check
Temporal smoothing
Time-window visibility check

## Slide 10: Framewise visibility | Patch visibility check
If is less than a threshold angle, the patch is visible. - In this work, we used 75 degrees as a threshold.
Framewise visibility check
Temporal smoothing
Time-window visibility check
Visible or Invisible

## Slide 11: Time-window visibility check
Calculate the visibility matrices of all the frames in the time-window.
If a patch is visible in all the frames, the patch is defined as visible during the time-window.
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
&
&
…
Frame 1
Frame n
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Visibility mask for
a time-window
(Visible or Invisible)
Framewise visibility check
Temporal smoothing
Time-window visibility check

## Slide 12: Experiments | PURE dataset
PURE: Pulse rate detection dataset [14]
  10 subjects, 60 seconds each.
  We used the most challenging medium rotation situation with 35 degrees head rotations
    Both 2D and 3D facial landmarks detection didn’t fail or lost in this situation.
Experimental procedures
  We cut videos into 10 sec. clips with sliding windows.
    In total 500 clips. (50 clips 10 subjects)
  Reference HR was obtained from beat-to-beat HRs (IBIs) calculated using a contact PPG sensor’s signal.
[14] R. Stricker et al., “Non-contact video-based pulse rate measurement on a mobile service robot,” ROMAN, 2014.

## Slide 13: Results | PURE dataset

## Slide 14: Results | PURE dataset
Improve!!
Our visibility check is effective.
Just replacing 2D with 3D is not enough.

## Slide 15: Results | PURE dataset
Improve!!
Our method outperforms the baseline method.

## Slide 16: Results | Tough rotation situation
2D facial landmarks
3D facial landmarks
Framewise visibility
Our method:
Successful estimation
Baseline method:
Inaccurate estimation

## Slide 17: Conclusion
We have proposed the first HR estimation method based on 3D facial landmarks.
We have proposed a novel face patch visibility check manner considering the 3D information.
We have experimentally demonstrated that our proposed method using the 3D landmarks outperforms the baseline method using the 2D facial landmarks.
Code is publicly available.
  http://www.ok.sc.e.titech.ac.jp/res/VitalSensing/3DfaceHR/index.html
Code is available.